WHAM
- Weighted Histogram Analysis Method
- Problem:
  - When simulations provide insufficient results over an entire region
- Solution:
  - Run biased simulations
  - Remove bias and combine simulation results to give results over entire region

---
Butane - Lighter Gas
Want to measure the energy (PMF) as a function of dihedral angle

---
Butane - PMF
- Unknown - Helps explain reactivity
- Can be measured with Molecular Dynamics (MD) Simulations
- Molecules favour regions of low energy
PMF
Dihedral Angel

---
PMF and Probability
High energy <=> Low Sampling Probability
Probability
Dihedral Angel

---
Umbrella Sampling
- Add an energy constraint to the MD simulation
- Constraint biases the simulation to run around a chosen angle

---
Umbrella Sampling
Adding the constraint at 40° biases simulation to red line
PMF
Dihedral Angel

---
Umbrella Sampling
MD Sampling Probability at 40°
Probability
Dihedral Angel

---
Umbrella Sampling
Samples at 40°
No. of
Samples
Dihedral Angel

---
Umbrella Sampling
Do this every 20 degrees
No. of
Samples
Dihedral Angel

---
- Values from simulations
  - Number of samples per bin for all histograms
  - Number of samples per histogram
  - Distribution bias applied
bar p^{o}_bar b = { sum from{s} n_{s,bar b} } over { sum from{s}N_s bar f_s c_{s, bar b}}
bar f_s = 1 over { sum from{bar b}c_{s,bar b} bar p^{o}_bar b}

---
- Puts all the results back together
  - Unknowns P and f
  - Start with all f = 1
  - Work out P
  - Work out f
  - Stop when difference f < 0.001
  - You are left with P
  - With P we can get PMF
bar p^{o}_bar b = { sum from{s} n_{s,bar b} } over { sum from{s}N_s bar f_s c_{s, bar b}}
bar f_s = 1 over { sum from{bar b}c_{s,bar b} bar p^{o}_bar b}

---
Final Probability (P)
Probability
Dihedral Angel

---
Final PMF (red line)
PMF
Dihedral Angel

---
- The approach
  - Generate test data
  - Develop WHAM implementations
    - CPU
    - GPU
  - Validate
  - Measure speed up against problem size

---
Test Data
- MD simulations are a dark art
- Test Harness
    - Generate samples from known reference PMF
    - Validate the WHAM generated PMF against known
This is artificial :
(2*(cos((6.1*pi*x)/360)
-1.2*(x/180)*(x/180))+4.38)

---
Generating Samples
Monte Carlo with Sampling Probability at 40°
Probability
Dihedral Angel

---
Validation
- Use Root Mean Square Deviation
    - Known Reference PMF
      against
    - WHAM generated PMF

---
- Implementations
  - Wrote a sequential version in Java
  - Then parallel versions
    - Java Multi Threading
    - Java Fork Join Framework
    - 3 - 4x speed on 8 CPU's up for small dataset

---
- Main optimization
  - Pre-compute and cache static values
bar p^{o}_bar b = { sum from{s} n_{s,bar b} } over { sum from{s}N_s bar f_s c_{s, bar b}}
bar f_s = 1 over { sum from{bar b}c_{s,bar b} bar p^{o}_bar b}

---
- Implementations
  - Wrote an optimised sequential version in C++
  - Then parallel version on GPGPU
    - Cached values only transferred once
    - Two kernels for block synchronization between equations
    - Mixed computation on GPU and CPU
    - Multi-dimensional support by flattening histograms

---
- Entire System

---
- Clojure benefits
  - Simulation config defined as code
  - Easy function composition and currying
  - Functions easily extended to n-dimensions
  - Availability of NDArray implementation.

---
- Results
  - Can vary number of dimensions, histograms and bins.
  - 20 2D test cases created
  - Best result:
    - 2D test case
    - 61 x 61 histograms and 180 x 180 bins
    - 120M elements
    - 19x speed-up